## Slide 1
Manure Gas Safety
Hydrogen sulfide exposures have killed livestock and farmers
People cannot smell when concentrations are dangerous
Hydrogen sulfide concentrations can increase quickly
Shows concentration of H2S gas
Lasts 2 years (hibernation case may extend lifetime)
BW Clip Real Time
SGC Plus
Shows months remaining; shows concentration when H2S is present
Lasts 2 years (IR link may extend lifetime)
Monitor Types
Monitors to measure hydrogen sulfide gas concentrations identify the risk in real time
Bump test the hydrogen sulfide monitor 2 weeks before and the start of the day you plan to do hazardous activities
Wear your hydrogen sulfide monitor near head or clipped onto collar
Turn on ventilation fans before manure handling activities
What can I do to reduce H2S risk?
Why should I be concerned about manure gas hazards?
Both vibrate, flash, and alarm
slow for low alarm
fast for high alarm

## Slide 2
For more, visit: www.gpcah.org
Monitor Use
High concentrations have been identified:
When pumping manure, inside and outside of buildings
After pumping is complete, inside buildings
During pressure washing
Inside full and empty manure storage pits
In unvented spaces with decaying materials
When hauling and land-applying manure
What Do the Numbers Mean?
Monitors alarm when concentrations reach levels that cause long-term health effects.
If monitor is alarming, ventilate the area and pay attention to concentration displayed on screen
Leave area immediately at 50 ppm
Concentrations may be deadly if monitor reads 100 ppm
Wear H2S monitor in high concentration areas